Trucks, Travel Gearing

Two, 4-wheel swiveling trucks, with 56 ½” gauge, support and transport the Ohio Locomotive Crane. Each truck is equipped with 33 inch multiple wear rolled steel car wheels pressed on forged steel axles.  Rubber load suspension packs eliminate potential spring breakage problems while minimizing longitudinal pitching and traverse rocking action.  Two 7 x 8 inch cylinders per truck provide the Ohio Crane with more than adequate braking power.  In addition a manually applied hand brake is furnished on one truck.

Flange-mounted to all welded steel gear cases, 115 H.P, traction motors provide the Ohio crane with smooth yet powerful traction performance.  Standard equipped cranes are capable of obtained a truck speed up to 15 mph.  An optional Field Shunting and 4-motor travel is also available should higher speeds be required.  Ohio’s standard quick travel gearing disengagement feature minimizes time required for preparing the Ohio crane for in-train transit

2

Carbody

Rugged all-welded extra heavy construction carbody’s give Ohio’s rock solid stability with no racking or twisting even under the heaviest of loads.  Standard built-in features include: removable Outrigger Plates, manually extended Heavy Beam Outriggers, Anti-Skid Deck Plates, A.A.R. approved Hand grabs and Footsteps and A.A.R. Type “E” Top Operated Couplers.